Experiment
- Nokia 6210/6310, CARC91, PC -

Author:	Jens Bennfors

Company	AB Indevia
Date:	2002-04-09

Contents

1.	Contents	2

2.	Introduction	3

3.	Setup	3

4.	Nokia 6210	4

4.1.	Phone connected to PC	4

4.1.1.	Initiation	4

4.1.2.	Incoming call	4

4.1.3.	Connected	4

4.1.4.	Initiation with connected phone	4

4.1.5.	Disconnected	5

4.1.6.	Incoming SMS	5

4.2.	Phone connected to CARC91	5

4.2.1.	Initiation	5

4.2.2.	Incoming call	5

4.2.3.	Connected	6

4.2.4.	Initiation with connected phone	6

4.2.5.	Disconnected	6

4.2.6.	Incoming SMS	6

4.2.7.	Button pushed	7

5.	Nokia 6310	8

5.1.	Phone connected to PC	8

5.1.1.	Initiation	8

5.1.2.	Incoming call	8

5.1.3.	Connected	8

5.1.4.	Initiation with connected phone	8

5.1.5.	Disconnected	9

5.1.6.	Incoming SMS	9

5.2.	Phone connected to CARC91	9

5.2.1.	Initiation	9

5.2.2.	Incoming call	10

5.2.3.	Connected	10

5.2.4.	Initiation with connected phone	10

5.2.5.	Disconnected	11

5.2.6.	Incoming SMS	11

5.2.7.	Button pushed	11

6.	Result	11

Introduction

The purpose of this experiment is to gain understanding about how Nokias commands for handsfree works in a way that can be of use in the construction of Com.n.sense. The means available is a Nokia 6210, a Nokia 6310, a HFU-2 CARC91 and a PC with a LabVIEW program installed.

Setup

I have connected the phone to a Nokia original handsfree (CARC91). I then use the PC for listening to the data communication between the phone and CARC91. I also send the frames directly from the PC to the phone.

Nokia 6210

Phone connected to PC

Initiation

1F0004 D0 0001 04 00CE			Power up from PC

1F0004 D0 0001 04 01CF			Power up from PC

1F0400 D0 0001 05 10DF			Power up from phone

1F0004 79 0005 0201 0164 00 0203 		Enable carkit mode from PC

1F0004 79 0005 0201 0164 00 0302		Enable carkit mode from PC

1F0400 7F 0367			Ack from phone

1F0004 79 0012 0201 0206 0056 2030 372E 3030 0A48 4655 3200 044F	  HFU-2 Version

1F0400 7F 0460			Ack from phone

1F0400 78 0004 0102 0801 117C		Status 0x08, 0x01 from phone

1F0400 78 0004 0102 0801 117C

1F0400 78 0004 0102 0801 117C

1F0400 DA 0002 0002 12D3			Type => 0xDA, data => 0x00, 0x02

1F0400 DA 0002 0002 12D3

1F0400 DA 0002 0002 12D3

1F0004 79 0005 0201 0164 00 0504 		Enable carkit mode from PC

1F0004 79 0005 0201 0164 00 0607		Enable carkit mode from PC

1F0400 7F 0662			Ack from phone

1F0004 78 0003 0201 0307 67 		Status confirm from PC

1F0004 78 0003 0201 0308 68		Status confirm from PC

1F0400 7F 086C			Ack from phone

The phone enters the profile ”handsfree” when the frame carkit enable is sent. It sends out an unknown status frame 0x08, 0x01.

Incoming call

1F0400 78 0004 0102 0701 197B		Status 0x07, 0x01 from phone

1F0400 78 0004 0102 0701 197B

1F0400 78 0004 0102 0701 197B

1F0400 78 0004 0102 0E03 1A73		Status 0x0E, 0x03 from phone

1F0400 78 0004 0102 0E03 1A73

1F0400 78 0004 0102 0E03 1A73

Status type 0x07 with status 0x01 means mute external audio equipment. Status type 0x0E with status 0x03 means audio amplifier on.

Connected

The phone doesn’t send out anything when a call has been set up.

Initiation with connected phone

1F0004 D0 0001 04 00CE			Power up from PC

1F0400 D0 0001 05 1BD4			Power up from phone

1F0004 79 0005 0201 0164 0001 00		Enable carkit mode from PC

1F0400 7F 0165			Ack from phone

1F0400 78 0004 0102 0E03 1C75		Status 0x0E, 0x03 from phone

1F0400 78 0004 0102 0E03 1C75

1F0400 78 0004 0102 0E03 1C75

1F0400 78 0004 0102 0701 1D7F		Status 0x07, 0x01 from phone

1F0400 78 0004 0102 0701 1D7F

1F0400 78 0004 0102 0701 1D7F

1F0004 79 0012 0201 0206 00 5620 3037 2E30 300A 4846 5532 00 0249  HFU-2 Version from PC

1F0400 7F 0266			Ack from phone

1F0400 78 0004 0102 0801 1E73		Status 0x08, 0x01 from phone

1F0400 78 0004 0102 0801 1E73

1F0400 78 0004 0102 0801 1E73

1F0004 79 0005 0201 0164 0003 02		Enable carkit mode from PC

1F0400 7F 0367			Ack from phone

1F0400 78 0004 0102 0E03 1F76		Status 0x0E, 0x03 from phone

1F0400 78 0004 0102 0E03 1F76

1F0400 78 0004 0102 0E03 1F76

1F0400 78 0004 0102 0701 2042		Status 0x07, 0x01 from phone

1F0400 78 0004 0102 0701 2042

1F0400 78 0004 0102 0701 2042

1F0004 78 0003 0201 03 0464		Status confirm from PC

1F0400 7F 0460			Ack from phone

Disconnected

1F04 0078 0004 0102 0700 2142		Status 0x07, 0x00

1F04 0078 0004 0102 0700 2142

1F04 0078 0004 0102 0700 2142

Incoming SMS

FCF0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0F0 F0				Initiation of bit length from phone

1F0400 78 0004 0102 0E03 254C		Status 0x0E, 0x03 from phone

F0F0F0F0

1F0400 78 0004 0102 0E03 254C

1F0400 78 0004 0102 0E03 254C

Phone connected to CARC91

Initiation

1F0004 D0 0001 04 00CE			Power up from HFU-2

1F0400 D0 0001 05 02CD			Power up from phone

1F0004 79 0005 0201 0164 00 0100		Enable carkit mode from HFU-2

1F0400 7F 0165			Ack from phone

1F0004 79 0012 0201 0206 0056 2030 372E 3030 0A48 4655 3200 0249  HFU-2 Version

1F0400 7F 0266			Ack from phone

1F0400 78 0004 0102 0801 036E		Status 0x08, 0x01

1F0004 79 0005 0201 0164 00 0302		Enable carkit mode from HFU-2

1F0400 7F 0367			Ack from phone

1F0400 78 0004 0102 0801 036E		Status 0x08, 0x01

1F0004 7F 0367			Ack from HFU-2

1F0400 DA 0002 0002 04C5			Status type => 0xDA, data => 0x00, 0x02

1F0004 7F 0460			Ack from HFU-2

1F0400 78 0004 0102 0E03 056C		Status 0x0E, 0x03

1F0004 7F 0561			Ack from HFU-2

1F0004 78 0003 0201 03 0464		Status confirm from HFU-2

1F0400 7F 0460			Ack from phone

1F0400 78 0004 0102 0E00 066C		Status 0x0E, 0x00

1F0004 7F 0662			Ack from HFU-2

1F0004 78 0003 0201 03 0565		Status confirm from HFU-2

1F0400 7F 0561			Ack from phone

Incoming call

1F0400 78 0004 0102 0701 1173		Status 0x07, 0x01

1F0004 7F 1175			Ack from HFU-2

1F0400 78 0004 0102 0E03 127B		Status 0x0E, 0x03

1F0004 7F 1276			Ack from HFU-2

1F0004 78 0003 0201 03 0868		Status confirm from HFU-2

1F0400 7F 086C			Ack from phone

Connected

The phone doesn’t send out anything when a call has been set up.

Initiation with connected phone

1F0004 D0 0001 04 00CE			Power up from HFU-2

1F0400 D0 0001 05 1AD5			Power up from phone

1F0004 79 0005 0201 0164 00 0100		Enable carkit mode from HFU-2

1F0400 7F 0165			Ack from phone

1F0400 78 0004 0102 0E03 1B72		Status 0x0E, 0x03

1F0004 79 0012 0201 0206 0056 2030 372E 3030 0A48 4655 3200 0249  HFU-2 Version

1F0400 7F 0266			Ack from phone

1F0004 79 0005 0201 0164 00 0302		Enable carkit mode from HFU-2

1F0400 7F 0367			Ack from phone

1F0400 78 0004 0102 0E03 1B72		Status 0x0E, 0x03

1F0004 7F 1B7F			Ack from HFU-2

1F0400 78 0004 0102 0801 1C71		Status 0x08, 0x01

1F0004 78 0003 0201 03 0464		Status confirm from HFU-2

1F0400 7F 0460			Ack from phone

1F0400 78 0004 0102 0801 1C71		Status 0x08, 0x01

1F0004 7F 1C78			Ack from HFU-2

1F0400 78 0004 0102 0E03 1D74		Status 0x0E, 0x03

1F0004 7F 1D79			Ack from HFU-2

1F0400 78 0004 0102 0701 1E7C		Status 0x07, 0x01

1F0004 78 0003 0201 03 0565		Status confirm from HFU-2

1F0400 7F 0561			Ack from phone

1F0400 78 0004 0102 0701 1E7C		Status 0x07, 0x01

1F0004 7F 1E7A			Ack from HFU-2

1F0400 78 0004 0102 0701 1F7D		Status 0x07, 0x01

1F0004 7F 1F7B			Ack from phone

1F0400 DA 0002 0002 20E1			Typ => 0xDA, data => 0x00. 0x02

1F0004 7F 2044			Ack from HFU-2

Disconnected

1F0400 78 0004 0102 0700 1774		Status 0x07, 0x00

1F0004 7F 1773			Ack from HFU-2

1F0400 78 0004 0102 0E00 1872		Status 0x0E, 0x00

1F0004 7F 187C			Ack from HFU-2

1F0004 78 0003 0201 03 0B6B		Status confirm from HFU-2

1F0400 7F 0B6F			Ack from phone

Incoming SMS

1F0400 78 0004 0102 0E03 076E		Status 0x0E, 0x03

1F0004 7F 0763			Ack from HFU-2

1F0004 78 0003 0201 03 0666		Status confirm from HFU-2

1F0400 7F 0662			Ack from phone

1F0400 78 0004 0102 0E00 0862		Status 0x0E, 0x00

1F0004 7F 086C			Ack from HFU-2

1F0004 78 0003 0201 03 0767		Status confirm from HFU-2

1F0400 7F 0763			Ack from phone

Button pushed

1F0400 78 0004 0102 0E03 0960		Status 0x0E, 0x03

1F0004 7F 096D			Ack from HFU-2

1F0004 78 0003 0201 03 0868		Status confirm from HFU-2

1F0400 7F 086C			Ack from phone

1F0400 78 0004 0102 0E00 0A60		Status 0x0E, 0x00

1F0004 7F 0A6E			Ack from HFU-2

1F0004 78 0003 0201 03 0969		Status confirm from HFU-2

1F0400 7F 096D			Ack from phone

Nokia 6310

Phone connected to PC

Initiation

1F0004 D0 0001 04 02CC			Power up from PC

1F0400 D0 0001 05 0DC2 			Power up from phone

1F0004 79 0005 0201 0164 00 0C0D 		Enable carkit mode from PC

1F0400 7F 0C68 			Ack from phone

1F0400 78 0004 0128 0B00 0E4B 		Status 0x0B, 0x00 from phone

1F0400 78 0004 0128 0B00 0E4B

1F0400 78 0004 0128 0B00 0E4B

1F0004 79 0012 0201 0206 0056 2030 372E 3030 0A48 4655 3200 0D46  HFU-2 version from PC

1F0400 7F 0E6A 			Ack from phone

1F0400 DA 0004 0028 0000 0FE2

1F0400 DA 0004 0028 0000 0FE2

1F0400 DA 0004 0028 0000 0FE2

1F0004 79 0005 0201 0164 00 1716		Enable carkit mode from PC

1F0400 7F 1773			Ack from phone

1F0400 78 0004 0128 0B00 1055		Status 0x0B, 0x00 from phone

1F0400 78 0004 0128 0B00 1055

1F0400 78 0004 0128 0B00 1055

1F0004 78 0003 0201 03 1878		Status confirm from PC

1F0400 7F 1A7E			Ack from phone

An unknown status frame (0x0B) is sent by the phone.

Incoming call

1F0400 78 0004 0128 0701 0D45 		Status 0x07, 0x01 from phone

1F0400 78 0004 0128 0E01 0F4E 		Status 0x0E, 0x01 from phone

1F0400 78 0004 0128 0A00 1054		Status 0x0A, 0x00 from phone

1F0400 78 0004 0128 0901 1157		Status 0x09, 0x01 from phone

Byte 8 in the status frames is some kind of ID number. 0x28 is the ID for 6310. Status 0x0A, 0x09 is unknown.

Connected

The phone doesn’t send out anything when a call has been set up. This might be because the profile “handsfree” is lost when ack isn’t sent.

Initiation with connected phone

1F0004 79 0012 0201 0206 0056 2030 372E 3030 0A48 4655 3200 1C57  HFU-2 version from PC

1F0400 7F 1C78			Ack from phone

1F0400 78 0004 0128 0E02 1A58		Status 0x0E, 0x02

1F0400 78 0004 0128 0A00 1B5F		Status 0x0A, 0x00

1F0400 78 0004 0128 0900 1C5B		Status 0x09, 0x00

1F0400 78 0004 0128 0701 1D55		Status 0x07, 0x01

1F0004 D0 0001 04 00CE			Power up from HFU-2

1F0400 D0 0001 05 74BB			Power up from phone

1F0004 79 0005 0201 0164 00 0100		Enable carkit mode from HFU-2

1F0400 7F 0165			Ack from phone

1F0004 79 0012 0201 0206 0056 2030 372E 3030 0A48 4655 3200 0249  HFU-2 Version

1F0400 7F 0266			Ack from phone

1F0400 78 0004 0128 0E01 7534		Status 0x0E, 0x01

1F0004 79 0005 0201 0164 00 0302		Enable carkit mode from HFU-2

1F0400 7F 0367			Ack from phone

1F0400 78 0004 0128 0E01 7534		Status 0x0E, 0x01

1F0004 7F 7511			Ack from HFU-2

1F0400 78 0004 0128 0A01 7633		Status 0x0A, 0x01

1F0004 7F 7612			Ack from HFU-2

1F0400 78 0004 0128 0901 7731		Status 0x09, 0x01

1F0004 7F 7713			Ack from HFU-2

1F0400 78 0004 0128 0701 7830		Status 0x07, 0x01

1F0004 7F 781C			Ack from HFU-2

1F0400 78 0004 0128 0E01 7938		Status 0x0E, 0x01

1F0004 7F 791D			Ack from HFU-2

1F0004 78 0003 2801 03 044E		Status confirm from HFU-2

1F0400 7F 0460			Ack from phone

1F0400 DA 0004 0028 0000 7A97		Type => 0xDA, data => 0x0028, 0x0000

1F0004 7F 7A1E			Ack from HFU-2

1F0400 78 0004 0128 0E01 7B3A		Status 0x0E, 0x01

1F0004 7F 7B1F			Ack from HFU-2

1F0400 78 0004 0128 0A00 7C38		Status 0x0A, 0x00

1F0004 78 0003 2801 03 054F		Status confirm from HFU-2

1F0400 7F 0561			Ack from phone

1F0400 78 0004 0128 0A00 7C38		Status 0x0A, 0x00

1F0004 7F 7C18			Ack from HFU-2

1F0400 78 0004 0128 0700 7D34		Status 0x07, 0x00

1F0004 7F 7D19			Ack from HFU-2

1F0400 78 0004 0128 0E00 7E3E		Status 0x0E, 0x00

1F0004 7F 7E1A			Ack from HFU-2

1F0004 78 0003 2801 03 064C		Status confirm from HFU-2

1F0400 7F 0662			Ack from phone

Disconnected

No response. Probably because phone has lost the profile “handsfree”.

Incoming SMS

1F0400 78 0004 0128 0E01 0849		Status 0x0E, 0x01

1F0400 78 0004 0128 0A00 094D		Status 0x0A, 0x00

1F0400 78 0004 0128 0901 0A4C		Status 0x09, 0x01

Phone connected to CARC91

Initiation

1F0004 D0 0001 04 00CE			Power up from HFU-2

1F0400 D0 0001 05 2DE2 			Power up from phone

1F0004 79 0005 0201 0164 00 0100		Enable carkit mode from HFU-2

1F0400 7F 0165			Ack from phone

1F0004 79 0012 0201 0206 0056 2030 372E 3030 0A48 4655 3200 0249  HFU version from HFU-2

1F0400 7F 0266			Ack from phone

1F0004 79 0005 0201 0164 00 0302 		Enable carkit mode from HFU-2

1F0400 7F 0367 			Ack from phone

1F0400 78 0004 0128 0E00 2E6E 		Status 0x0E, 0x00

1F0004 7F 2E4A 			Ack from HFU-2

1F0004 78 0003 2801 03 044E		Status confirm from HFU-2

1F0400 7F 0460			Ack from phone

1F0400 DA 0004 0028 0000 2FC2

1F0004 7F 2F4B			Ack from HFU-2

Incoming call

1F0400 78 0004 0128 0701 3078		Status 0x07, 0x01

1F0004 7F 3054			Ack from HFU-2

1F0400 78 0004 0128 0701 3179		Status 0x07, 0x01

1F0004 7F 3155			Ack from HFU-2

1F0400 78 0004 0128 0E01 3273		Status 0x0E, 0x01

1F0004 7F 3256			Ack from HFU-2

1F0400 78 0004 0128 0A00 3377		Status 0x0A, 0x00

1F0004 78 0003 2801 03 054F		Status confirm from HFU-2

1F0400 7F 0561			Ack from phone

1F0400 78 0004 0128 0A00 3377		Status 0x0A, 0x00

1F0004 7F 33 57			Ack from HFU-2

1F0400 78 0004 0128 0901 3472		Status 0x09, 0x01

1F0004 7F 3450			Ack from HFU-2

Connected

1F0400 78 0004 0128 0E01 3574		Status 0x0E, 0x01

1F0004 7F 3551			Ack from HFU-2

1F0400 78 0004 0128 0A01 3673		Status 0x0A, 0x01

1F0004 78 0003 2801 03 064C 		Status confirm from HFU-2

1F0400 7F 0662			Ack from phone

1F0400 78 0004 0128 0A01 3673		Status 0x0A, 0x01

1F0004 7F 3652			Ack from HFU-2

1F0400 78 0004 0128 0A00 3773		Status 0x0A, 0x00

1F0004 7F 3753			Ack from HFU-2

1F0400 78 0004 0128 0900 387F		Status 0x09, 0x00

1F0004 7F 385C			Ack from HFU-2

1F0400 78 0004 0128 0A01 397C		Status 0x0A, 0x01

1F0004 7F 395D			Ack from HFU-2

1F0400 78 0004 0128 0901 3A7C		Status 0x09, 0x01

1F0004 7F 3A5E 			Ack from HFU-2

Initiation with connected phone

1F0004 D0 0001 04 00CE			Power up from HFU-2

1F0400 D0 0001 05 5996			Power up from phone

1F0004 79 0005 0201 0164 00 0100		Enable carkit mode from HFU-2

1F0400 7F 0165			Ack from phone

1F0004 79 0012 0201 0206 0056 2030 372E 3030 0A48 4655 3200 0249  HFU-2 Version

1F0400 7F 0266			Ack from phone

1F0400 78 0004 0128 0E01 5A1B		Status 0x0E, 0x01

1F0004 79 0005 0201 0164 00 0302		Enable carkit mode from HFU-2

1F0400 7F 0367			Ack from phone

1F0400 78 0004 0128 0E01 5A1B		Status 0x0E, 0x01

1F0004 7F 5A3E			Ack from HFU-2

1F0400 78 0004 0128 0A01 5B1E		Status 0x0A, 0x01

1F0004 7F 5B3F			Ack from HFU-2

1F0400 78 0004 0128 0901 5C1A		Status 0x09, 0x01

1F0004 7F 5C38			Ack from HFU-2

1F0400 78 0004 0128 0701 5D15		Status 0x07, 0x01

1F0004 7F 5D39			Ack from HFU-2

1F0004 78 0003 2801 0305 4F		Status confirm from HFU-2

1F0400 7F 0561			Ack from phone

1F0400 DA 0004 0028 0000 5EB3

1F0004 7F 5E3A			Ack from HFU-2

Disconnected

1F0400 78 0004 0128 0E01 3B7A 		Status 0x0E, 0x01

1F0004 7F 3B5F 			Ack from HFU-2

1F0400 78 0004 0128 0A00 3C78 		Status 0x0A, 0x00

1F0004 78 0003 2801 03 074D		Status confirm from HFU-2

1F0400 7F 0763			Ack from phone

1F0400 78 0004 0128 0A00 3C78		Status 0x0A, 0x00

1F0004 7F 3C58			Ack from HFU-2

1F0400 78 0004 0128 0700 3D74		Status 0x07, 0x00

1F0004 7F 3D59			Ack from HFU-2

1F0400 78 0004 0128 0E00 3E7E		Status 0x0E, 0x00

1F0004 7F 3E5A			Ack from HFU-2

1F0004 78 0003 2801 0308 42		Status confirm from HFU-2

1F0400 7F 086C			Ack from phone

Incoming SMS

1F0400 78 0004 0128 0E01 6627		Status 0x0E, 0x01

1F0004 7F 6602			Ack from HFU-2

1F0004 78 0003 2801 03 064C		Status confirm from HFU-2

1F0400 7F 0662			Ack from phone

1F0400 78 0004 0128 0E00 6727		Status 0x0E, 0x00

1F0004 7F 6703			Ack from HFU-2

1F0004 78 0003 2801 03 074D		Status confirm from HFU-2

1F0400 7F 0763			Ack from phone

Button pushed

1F0400 78 0004 0128 0E01 0948		Status 0x0E, 0x01

1F0004 7F 096D			Ack from HFU-2

1F0004 78 0003 2801 03 064C		Status confirm from HFU-2

1F0400 7F 0662			Ack from phone

1F0400 78 0004 0128 0E00 0A4A		Status 0x0E, 0x00

1F0004 7F 0A6E			Ack from HFU-2

1F0004 78 0003 2801 03 074D		Status confirm from HFU-2

1F0400 7F 0763			Ack from phone

Result

Important things to consider when designing a program for Com.n.sense that is to work with 6310.

- 6310 sends out status 0x0E, 0x01 when speaker should be enabled

- HFU-2 version has to be sent in order for 6310 to switch to profile ”Handsfree”.

- Status 0x0A might say weather the phone is ringing or connected. Only 6310 send this status.

- Status confirm should be sent when status 0x0E is received.